## Slide 1
TOWN OF BERTHOUD MS4 COMPLIANCE AND ENFORCEMENT PROGRAM draft created 9/24/23 & updated 10/26/23
1. Grading and Erosion Control (GESC) Permit Form – Online
2. Applicant Submits Permit via Community Core
6. Inspection
5. Initial Erosion Control Measures Installed
For public improvement work, surety is provided in compliance with the Development Agreement. For Building Permits Payment is made via Counter or Call
3. Staff Performs Completeness Review
If reviewed and approved under a Subdivision Review Process, Engineering to confirm that a Development Agreement is in place and Move to Step 4
Building to issue a stop work order if applicant fails to comply. Penalty payment = 2x the permit fee
4. Permit is accepted
Community Core generates invoice & emails applicant
Engineering to schedule on-site pre-construction meeting [Site-specific development plans and Subdivisions only]
Inspections are performed either by Engineering for Subdivision Improvements or by Building for Building Permits
7. Building Permit Issuance or Warranty Start
Failed Inspections require repair within 48 hours, or time determined by inspector
Inspections occur during duration of construction
Repeat inspection fees?
Inspection Reporting Form to be kept on-site during entire length of construction. Contractor to maintain accurate and up-to-date records of all permits, plans, inspections, and corrective actions taken. This documentation is vital for demonstrating compliance during any regulatory audits.
Incomplete applications are returned
If disturbance > 0.5 acres or part of a larger common plan = Town – issued Stormwater Quality Permit [aka Grading and Erosion Control Permit]
If disturbance > 1 acre = State Stormwater Permit Certification
Erosion Control Plans will be reviewed by Engineering through site-specific development review processes. Small-site erosion control is reviewed through the Building Permit process.
Town Process
Town Stormwater Quality Permit
No land disturbance allowed prior to installation of permitter controls
Final Landscape or stabilization measures and drainage installed and inspected
&